## Slide 1: Battery Circuit

## Slide 2: Idea
Lithium batteries are finicky and need current regulators and overcharge protections to charge safely
One cell batteries are much easier to get and much cheaper. Boosting voltage to 5V is needed for 5V logic circuits.
Charging ICs use current to determine if battery is charged or not. To accomplish this the load should be disconnected when DC power is given to the instrument. A p-MOSFET IC is a nice solution to this.

## Slide 3: Common breakout board
Breakout board are nice references as they are inclusive units. Here is a common schematic of one.
We have the TP4056 chip currently, but are missing the over voltage protection IC and the N-MOSFET which I believe switches power on and off to the battery as needed (not certain here). Here is a video about it: https://www.youtube.com/watch?v=Fj0XuYiE7HU
Also no temp protection is needed as it will be used in room temp situations.

## Slide 4: Load switching
We need to disconnect the battery when DC power is added so that the DC power runs the device and separately charges the battery.
This is an article about the issue: https://www.best-microcontroller-projects.com/tp4056-page2.html. Basically, one p-MOSFET disconnects the battery from load circuit. The other disconnects the DC from the load circuit. If hooked up in a certain way, it will make sure only one if connected to the load at a time and at the same time, the battery and DC are not connected directly themselves.
AO4803A is a dual channel p-mosfet which appears suitable for load switching according to its data sheet.